## Slide 1: RL for LEO Satellite Momentum Stabilization
Anirudh Aatresh, Joseph Breeden, Kevin Tan, Liliang Wang

## Slide 2: Introduction: The Problem
Space is not a vacuum, especially for satellites in Low Earth Orbits (LEO)
Disturbances include
  Upper atmospheric drag, solar radiation pressure, gravity gradient, magnetic field interactions
These disturbances
  Induce orbit decay
  Rotate the satellites
Even worse for tiny CubeSats

## Slide 3: Countering the Problem
Onboard reaction wheels can be used to counter the rotation induced by the disturbances
Must be regularly unloaded to prevent saturation
Solution:
  Use Earth’s magnetic field to provide an opposing torque while unloading stored momentum in the wheels
  Existing control laws not robust to irregularities in the Earth’s magnetic field and CubeSat construction limitations
  Use RL to create a new control law robust to these
Experiments will be based on a simulated environment developed by NASA called 42

## Slide 4: Mathematical Formulation
Let the CubeSat’s position be described by the angles relative to the positions of the Earth and the Sun
  is the position of the satellite in the orbit
  is the precession of the orbit
  is the angle between the local Sun vector and the normal vector to the orbital place
  , where is the current rotation of the Earth in the day

## Slide 5: State Space, Control, Dynamics
If the reaction wheels perfectly account for all disturbances and the CubeSat altitude is fixed, the wheel dynamics are:
  is the stored momentum on each axis of the satellite
  The disturbance torque due to drag, , is a function of the position and unknown parameters
  is the current orbit’s normal vector and and are constants
  , the magnetic torque, satisfies , where is the the commanded satellite magnetic field (our control input)
  We can only control two axes at once, and require
  is the magnetic field of the Earth at the current point
The state space is , and the objective is to minimize throughout the entire orbit

## Slide 6: Satellite Disturbances
The atmosphere changes slowly but in unpredictable ways
= measure of current solar activity
= measure of current geomagnetic activity
High activity  denser atmosphere  more disturbances
These indices are frequently measured in daily/hourly timescales
Result: disturbances are not random on short time-scales
  Question: what are the best choices of to train and evaluate the policies?

## Slide 7: One Orbit
CubeSat orientation is fixed
Simulates mid-fidelity disturbance models with specified

## Slide 8: Method
Linear control laws are inefficient due to the complexity of the Earth’s magnetic field
  Baseline algorithm requires unrealistically large momentum storage capacity
We use actor-critic based algorithms to train a controller to choose a series of actions to drive the angular momentum of the wheels close to zero:
  Successfully transfer the momenta of the reaction wheels to the Earth through magnetic actuators interacting with the Earth’s magnetic field

## Slide 9: Online or Offline?
We look towards solving this problem offline
  Leaves open the possibility of learning a policy on real satellite data in the future, not just data from 42
  Allows for offline pre-training, allowing for more effective policies when combined with online policy improvement
  Learning a policy online from scratch in the context of a real satellite will be dangerous and costly
Data will be collected from 42 from two behavior policies
  Stochastic policy
  Decent baseline policy

## Slide 10: Offline RL
Online RL
  Get state, take action, observe next state
  Learning by doing
Off-policy RL
  Get state, take action based on behavior policy, observe next state
  Update new policy in the background
Offline RL
  Observe a dataset of states, actions, rewards collected by a behavior policy
  Learning by watching someone else do the doing

## Slide 11: d3rlpy: An Offline Deep RL Library
Offline reinforcement learning library
State-of-the-art algorithms
Scikit-learn style API

## Slide 12: Algorithms we Tried
Learning
  Conservative Q-Learning (CQL)
    Promising algorithm performing offline soft actor-critic computation with a modified Q-function estimator
    Tackles the common problem of overestimating the Q-value in offline RL
  TD3 + BC
    TD3, but imposing a penalty on actions different from the behavior policy
  Conservative Offline Model-Based Policy Optimization (COMBO)
    Fit a probabilistic dynamics model on observed data and generate synthetic data
    Train on synthetic data with regularization on out-of-sample state-action tuples
Off-Policy Evaluation
  Fitted Q-Evaluation
    Fit a Q-function with mean-square TD error loss on the collected dataset

## Slide 13: Conservative Q-Learning
Applicable to continuous state-action control problem
Suitable for complex and multi-modal data distribution
Addresses the common issue of standard offline RL algorithms:
Overestimation of value function

## Slide 14: Conservative Q-learning for Offline RL
Motivation:
  Overestimation induced by:
    Distributional shift between the behavior policy and the learned policy
    Function approximation error
Solution:
  Learn conservative, lower-bound estimates of the value function by
  regularizing the Q-values during training

## Slide 15: Conservative Q-learning for Offline RL
Conservative off-policy evaluation
Where,
Operator:
given a dataset
Empirical control policy:
Tradeoff factor:
Theorem: when

## Slide 16: Conservative Q-learning for Offline RL
Conservative Q-learning
: regularizer, and

## Slide 17: Conservative Q-learning for Offline RL
Algorithm

## Slide 18: TD3+ BC (Behavior Cloning)
TD3's policy is updated with the deterministic policy gradient:
TD3+BC: add a behavior cloning term to regularize the policy:

## Slide 19: Fitted-Q Evaluation

## Slide 20: Preliminary Experiments: Small Dataset
Four orbits of training data
Four orbits used for evaluation via FQE
Deterministic baseline: -4.1
Stochastic baseline: -5.63
 | FQE | 
 | Evaluation on data generated through stochastic policy | Evaluation on data generated through deterministic policy
CQL trained on data collected using the stochastic policy | -1.046 | -1.3
CQL trained on data collected using the deterministic policy | -1.263 | -1.658
TD3+BC trained on data collected using the stochastic policy | -1.067 | -0.826
TD3+BC trained on data collected using the deterministic policy | -1.751 | -1.724
COMBO trained on data collected using the stochastic policy | -1.687 | -1.453
COMBO trained on data collected using the deterministic policy | -2.243 | -1.104

## Slide 21: Hyperparameter Tuning
Hyper-parameters are those quantities that are set or initialized prior to training and aid in learning the parameters of the model in focus.
These quantities are not fit during training
The hyper-parameters that we varied in our initial experiments are:
  Learning rate of actor
  Learning rate of critic
  Learning rate of temperature (for CQL)
  Number of steps in TD calculation
  Discount factor.
Trained on a small dataset for 100 epochs and evaluated over 100 epochs.

## Slide 22: Hyperparameter Tuning
 | Hyper parameters |  |  |  |  | FQE | 
 | Learning rate of actor | Learning rate of critic | Learning rate of temperature parameter (CQL only) | Number of steps in TD Calculation | Discount factor | Evaluation on data generated through stochastic policy | Evaluation on data generated through deterministic policy
CQL trained on data collected using the stochastic policy | 1.00E-05 | 3.00E-04 | 1.00E-04 | 1 | 0.99 | -1.046 | -1.3
 | 1.00E-05 | 3.00E-04 | 1.00E-04 | 3 | 0.99 | -0.788 | -1.178
 | 1.00E-04 | 3.00E-04 | 1.00E-04 | 3 | 0.99 | -0.991 | -1.321
CQL trained on data collected using the deterministic policy | 1.00E-05 | 3.00E-04 | 1.00E-04 | 1 | 0.99 | -1.263 | -1.658
 | 1.00E-05 | 3.00E-04 | 1.00E-04 | 3 | 0.99 | -1.333 | -1.404
 | 1.00E-05 | 3.00E-04 | 1.00E-04 | 5 | 0.99 | -1.105 | -1.171
TD3+BC trained on data collected using the stochastic policy | 1.00E-05 | 3.00E-04 | - | 1 | 0.99 | -1.067 | -0.826
 | 3.00E-05 | 3.00E-04 | - | 1 | 0.99 | 0.708 | -2.948
 | 1.00E-05 | 3.00E-04 | - | 3 | 0.99 | -1.371 | -0.887
TD3+BC trained on data collected using the deterministic policy | 1.00E-05 | 3.00E-04 | - | 1 | 0.99 | -1.751 | -1.724
 | 3.00E-05 | 3.00E-04 | - | 1 | 0.99 | -1.522 | -1.742
 | 1.00E-05 | 3.00E-04 | - | 3 | 0.99 | 0 | 0

## Slide 23: Moving it to 42: Evaluating Policies Online
Pipeline
  Run 42 several times to generate training data
  Import data into d3rlpy
  Run various training algorithms
  Export neural net policy
  Import neural net policy into C++ program using torchscript (beta)
  Evaluate new policy in 42
Notes: Writing that C++ program took a very long time

## Slide 24: Policy Performance
Nominal Case:
  F10.7 index = 180,
  AP index = 70 (same as prior plot)
  100 chunks
No Control Input
PID Control Input
CQL – PID Training Data
CQL – Stochastic Training Data

## Slide 25: Policy Control Inputs
Nominal Case:
  F10.7 index = 180,
  AP index = 70
  100 chunks
No Control Input
PID Control Input
CQL – PID Training Data
CQL – Stochastic Training Data

## Slide 26: Conclusions – Nominal Environment
RL does not prevent divergence, but decreases average system momentum
RL uses similar control inputs even when trained with purely stochastic data
How much data is necessary?
  Somewhere between 4 and 100 “chunks”
Performed better than PID even with a PID behavior policy
Control inputs do not saturate, which means additional control authority is available

## Slide 27: Training on Smaller Dataset
Only 4 chunks
Results likely heavily dependent on what disturbances were observed during these chunks
CQL – PID Training Data
CQL – Stochastic Training Data

## Slide 28: Training on Smaller Dataset
Need more chunks to give a good evaluation of these methods
TD3+BC – Stochastic Training Data
TD3+BC – PID Training Data

## Slide 29
Training on Smaller Dataset
Need more chunks to give a good evaluation of these methods
COMBO – Stochastic Training Data

## Slide 30: Policy Performance for Off-Nominal Environment
Strong Disturbance:
  F10.7 index = 230,
  AP index = 100
  100 chunks
This case is at the edge of the training set
No Control Input
PID Control Input
CQL – PID Training Data
CQL – Stochastic Training Data

## Slide 31: Policy Performance for Off-Nominal Environment
Weak Disturbance:
  F10.7 index = 140,
  AP index = 40
  100 chunks
RL controllers are too aggressive
No Control Input
PID Control Input
CQL – PID Training Data
CQL – Stochastic Training Data

## Slide 32: Policy Performance for Off-Nominal Environment
Weak Disturbance:
  F10.7 index = 140,
  AP index = 40
  100 chunks
RL controllers are too aggressive
No Control Input
PID Control Input
CQL – PID Training Data
CQL – Stochastic Training Data

## Slide 33: Long Term Policy Performance
Nominal case
RL control laws are not effective outside of the training set (first 5500 seconds)
CQL – PID Training Data
No Control Input
PID Control Input
CQL – Stochastic Training Data

## Slide 34: Comparison to Fitted Q Evaluation
Consider CQL algorithm trained with PID behavior policy
PID total reward = -7.5
FQE based on training = –1.38
Real reward in 42 = –4.0
FQE is optimistic
  This is not entirely fair because of the way disturbances are introduced

## Slide 35: Training Improvements
Less frequent state sampling (e.g. every 2 seconds)
  Avoid data overload!
Vary the disturbance level throughout an orbit
  Not realistic but may yield more stable training results
Cover wider state space area, including diverging states
Train with new hyperparameters
Different neural network structures
  Current neural net was very simple (2 layers, 256 elements)

## Slide 36: Limitation
Unknown parameters
= measure of current solar activity
= measure of current geomagnetic activity
High activity  denser atmosphere  more disturbances
These indices are frequently measured in daily/hourly timescales
Result: disturbances are not random on short time-scales
  Fixed at the start of each episode
Global confounder! We’re dealing with offline confounded RL

## Slide 37: Steps Moving Forward
Generate training data for multiple orbits (i.e. all state angles)
Test different algorithms
Use improved hyperparameters
Determine required data quantity

## Slide 38: Questions
Comments